## Slide 1: Near Surface Geophysics as Used in Geotechnical Site Investigations
Presented by
Simon Hughes

## Slide 2: About me

## Slide 3: Talk Contents
What is geophysics?
Benefits and advances in use
Case study – mine shafts
Case study - bypass
Case study – pipelines
Case study – wind farm
Other techniques

## Slide 4: WHAT IS GEOPHYSICS?
We need a RADAR survey – can you do it yesterday?

## Slide 5: Geophysics is a magical black box!
Unintelligible pages of numbers
Too expensive
Unreliable
Inaccurate
Slow

## Slide 6
“…a suite of measurement techniques that can be used to precisely measure physical properties
of the subsurface and the contrast with the target”
chargeability thermal conductivity resistivity seismic radioactivity velocity density magnetism electrokinesis dielectricity acoustic mass electromagnetic

## Slide 7: Benefits of using geophysics

## Slide 8: 1: Non-invasive
“Ability to measure subsurface properties without need for excavation or drilling”
Ideal for urban / developed sites
Can be used on SSSIs
No reinstatement costs

## Slide 9: 2: Total site coverage
Where would you drill?

## Slide 10: 2: Total site coverage
You may have missed the solution feature!

## Slide 11: 3: Overcome errors in geological interpolation
“Geophysical data is continuous over a site or along a profile”
Avoids misinterpretation of bedrock e.g. borehole down fracture or into boulder

## Slide 12: 4: Low risk to site operatives from hazards
Pipelines or cables
Soft ground
Shafts or wells
Chemical contamination
Unexploded ordnance
Voids and caverns
Able to work on sensitive sites
No risk of cross-contamination through excavation

## Slide 13: Recent advances
“Old” geophysics…
Slow
Non-portable
Analogue
Lower Resolution
Today’s methods based on same principles but…
Faster
Higher Resolution
More portable
Much more cost effective
1950 Megger Resistivity System

## Slide 14: Recent advances
GPS positioning – greater speed & anomaly positioning

## Slide 15: Recent Advances:
GIS and 3D integration of geophysics with other sources of data e.g.
Surveying
Historical
Geochemical
Geological
Aerial Photos
Notes: Smaller, lighter instrumentation
Digital acquisition and storage
Real-time data display
Faster acquisition = higher resolution
GPS positioning
Increasing use in Industry
Improved Software Analysis

## Slide 16: Recent Advances:
In-field analysis of data
Positioning of anomalies
Data QA
Optimal parameters

## Slide 17: When to use geophysics?
Desk study
Site visit
GEOPHYSICS
Optimal design for borehole / sampling
Integration of data
Final conclusions

## Slide 18: Issues with geophysics!
Poorly written spec.
Poor site conditions
Poor data quality
Poorly presented results
Wrong methods used
Lack of understanding

## Slide 19: CASE STUDIES

## Slide 20: Case Study - mine shafts
Aim: to locate mineshaft under playing field for
school extension
Techniques:
conductivity
magnetic
microgravity

## Slide 21: EM Conductivity
Background
Induced electromagnetic field gives measure of subsurface electrical conductivity to depths of 0.5-60 metres. Variation in conductivity due to: clay minerals, metal, water saturation, void space
Common Applications:
Shallow geology
Contamination plumes
Foundations and services
Buried pits or infilled quarries
Limitations
Noise from services / buildings

## Slide 22: Magnetics
Theory:
“passive measurement of anomalies in the Earth’s magnetic field cause by buried ferrous objects”
Common Applications:
USTs and drums
UXO
Archaeology
Limitations:
Noise from services / buildings
Non-ferrous metal targets

## Slide 23: Microgravity
Theory: “Passive measurement of subtle variations in Earth’s gravity due to subsurface density changes caused by voids or different geological compositions.”
Common Applications:
Void and fissure mapping
Buried basements
Abandoned mine workings
Buried valleys
Limitations:
Acoustic noise & vibrations, wind, earthquakes
Speed of acquisition

## Slide 24: Case Study - mine shaft

## Slide 25: Case Study - mine shaft

## Slide 26: Case Study - mine shaft

## Slide 27: Case Study - bypass
Aim: to locate solution features along route of proposed bypass.
Technique: resistivity and follow-up microgravity if needed

## Slide 28: Resistivity
Theory: “ground resistance in relation to an induced DC electrical field is measured using electrode array.”
Common Applications:
bedrock profiling
buried channel mapping
overburden characterisation
landfill characterisation
Limitations:
Buried conductors e.g. rebar or cables
Geographical obstructions e.g. walls, cliffs

## Slide 29: Case Study - bypass

## Slide 30: Case Study - bypass

## Slide 31: Case Study - pipeline
Aim: map bedrock profile for directional drilling
Techniques: resistivity and seismic

## Slide 32: Seismic refraction
Theory: “measurement of subtle variations in the seismic velocity of subsurface materials”
Common Applications:
bedrock profiling
rock rippability
water table mapping
Limitations:
Acoustic noise / on site activity
Poor velocity contrast

## Slide 33
P wave refraction
- Rippability
S wave refraction
- Shear modulus and rock head
MASW
- Shear velocities and bulk data
A seismic section
(right) provides
detailed lateral
model for a
proposed
pipeline.
P wave refraction with
MASW (Stiffness) plot overlaid
- MASW often used in conjunction
with P + S wave due to its
ability to derive bulk values.

## Slide 34: Seismic refraction

## Slide 35: Case Study - pipeline

## Slide 36: Case Study - pipeline

## Slide 37: Case Study – wind farm
Aims: map depth to bedrock, geotechnical
properties for foundation design and soil
resistivity for earthing
Techniques: seismic and resistivity

## Slide 38: Case Study – wind farm

## Slide 39: Case Study – wind farm

## Slide 40: Case Study – wind farm

## Slide 41: Case Study – wind farm
Seismic data
Soil resistivity
data

## Slide 42: Techniques not covered

## Slide 43: Techniques not covered - GPR

## Slide 44: Techniques not covered – borehole seismic
Theory: Shooting either between boreholes (cross-hole) or from surface to borehole (down-hole)
Common Applications:
Caves/stopes/adits
Engineering properties
fracture zones
Buried valleys
Limitations:
Acoustic noise & vibrations
Bore hole separation distance (4.5 – 6 m)

## Slide 45: Techniques not covered – borehole seismic

## Slide 46: Techniques not covered – new!

## Slide 47: You need a geophysical survey?
Aims and why - depth, size and nature of targets if known?
Size of the site?
Site cover (vegetated, building, rebar…)?
Geological setting?
Geographical setting?
Any existing desk study data?
Access limitations?

## Slide 48: The End